## Slide 1
PRS tools
problem, risk, safety
General:
The PRS (Problem, risk, safety) family includes various tools:
problem solving method
risk management
preservation of safety
Some tools are specific and related to ISO 31000 and ISO 45001 standards, others are of universal application.
List of tools:
5 W
8 D
A 3
Brainstorming
DMAIC, define, measure, analyze, improve, control
FMEA, failure mode and effect analysis
FTA, fault tree analysis
HACCP, hazard analysis and critical control points
HAZOP, hazard and operability study
Maslow’s pyramid
PESTEL analysis, political, economical, social, legal, environmental, technological
Preliminary hazard analysis
RCA, root cause analysis
Risk level
Scenario analysis
SWIFT, structured « What-if » techniques
SWOT analysis, strengths, weaknesses, opportunities, threats
The single document
WWWWHHW, who, what, where, when, how, how much, why

## Slide 2
Description:
Problem solving method. The 5 W tool, (5 times why) allows you to find the root cause of a problem by asking five times the question "Why?". Children often do it!
Edwards Deming said: "If you do not know how to ask the right question, you discover nothing."
When the root cause is identified, put in place a solution to prevent a recurrence of the problem.
Interests:
Go easily at root cause.
Differentiating effects from causes.
Definitively eradicate the root cause.
W1
Why has the fuse blown?
Because the current was too high!
Why was the current too
high?
Because the engine had overheated!
Why had the engine overheated?
Because the bearing was worn!
Why was the bearing worn?
Because dust had entered!
Why had dust entered?
Because the cover was cracked!
W2
W3
W4
W5
  1 5 W
Example of engine failed:
Conclusion: we must change the bearing and change or reinforce the cover!
Tip: when the answer is not forthcoming it's because we approach the root cause
problem, risk, safety

## Slide 3
Interests:
Immediate actions allow to reassure the customer on the specific case.
Capitalization to other products or processes of lessons learned enables continuous improvement of skills of the company.
Description:
Problem solving method. The 8 D tool (8 times do) was applied at the beginning to customer returns in the automotive industry.
This is a team effort combining the best skills available. When the definitive actions are implemented and the results are positive without any adverse effect, the 8 D report is closed, recorded and sent to the customer.
D1
Build the multidisciplinary team with leader and participants. Objectives, roles, responsibilities
Describe in detail the problem with supporting figures (WWWWHHW, 5W, 5 M tools)
Identify immediate actions to be put in place to isolate the problem. Measure the effectiveness of actions
Identify the root causes behind the effects (5 W, brainstorming, Ishikawa diagram tools)
Choose permanent corrective actions. Estimate the effectiveness of actions and the absence of adverse effects
Plan and implement the long-term corrective actions. Check the effectiveness of actions
D2
D3
D4
D5
D6
Avoid renewal of problem. Change the documentation. Standardize good practices
D7
  2 8 D
problem, risk, safety
Communicate the team's efforts. Praise Team
D8
Method:

## Slide 4
Description:
Problem solving problem. The name A 3 comes from page dimensions A 3 (29.7 x 42 cm), very wise format for quick and synthetic operational management tool.
Visual communication report, part of the dashboard containing key information on the situation.
Manual update by participants of the multidisciplinary team.
Interests:
The focus is on the P stage of the PDCA (1 to 5).
Synthetic method to find the root causes of the problem.
Makes sure that the problem does not re-appear.
Promotes teamwork to solve problems together.
1
Build the team and name the leader. Clarify the problem. Use colors
Establish the initial context in the field. Use images, photos, figurines
Define the objective to achieve
Stir your brain and identify the root causes (5 W, Ishikawa diagram)
Analyze the causes, choose the best solution and establish the action plan (who, what, when, where, how)
Implement the actions. Try, if necessary, several times
2
3
4
5
6
Verify the effectiveness of actions. Analyze the results. Standardize good practices
7
  3 A 3
problem, risk, safety
Method:

## Slide 5
Description:
Problem solving method. Collective team tool and choice of ideas to research opportunities for improvement in pleasant conditions.
Rules:
propose as many ideas as possible
no censorship or personal criticism
do not be afraid or ashamed to speak freely
bounce back positively on the ideas
one idea = one post-it
do not to speak simultaneously
Interests:
Quickly collect many ideas and suggestions.
Find possible causes.
Imagine different solutions and new tracks.
Promotes and strengthens team spirit.
Fosters creativity, staff involvement.
1
Build the team. Determine the subject to be treated. Remember the "rules of the game"
Ask the questions in turn and collect ideas
Sort ideas into families (post-it on the blackboard)
Delete duplicates and irrelevant ideas
Ask every one to note all the ideas as an example from 1 to 10
Identify the top 3. Conclude with a discussion on best ideas
2
3
4
5
6
  4 Brainstorming
problem, risk, safety
Method:

## Slide 6
Description:
Problem solving method. The DMAIC (define, measure, analyze, improve, control) is a team-based tool seeking opportunities for improvement and statistical data. We can consider this method as a variant of the PDCA cycle with a P step reinforced.
Interests:
Deepening a problem and finding the right solution.
Check solution thanks to:
confrontation of ideas within the team
statistical data used and
tests
D
Build the team. Define the problem. Set goals. Identify what is important to the customer. Estimate the savings that will be realized.
Determine what you will measure. Confirm the measurement means. Choose a key indicator to measure. Measure the current process performance (capability). Estimate potential improvement.
Analyze the root causes of variability. Use of the verified data obtained in the field.
Innovate and improve the process with the new solution. Check that there is no statistically adverse effects.
Check the effectiveness of solutions. Hold enhanced process performance. Update documentation.
M
A
I
C
  5 DMAIC
problem, risk, safety
Method:

## Slide 7
1
Build the team. Find consensus on listing indexes
Perform functional analysis of needs and technical functional analysis
Identify the activities and their modes and failure effects
Determine the severity indexes of the effects, the frequency of occurrence of the causes and the risk of their non-detection
Calculate and classify all critical points by priority
For every high criticality plan actions with responsible, objective and deadline
2
3
4
5
6
Review the monitoring of actions. If the new criticality is high repeat the FMEA
7
  6 FMEA
problem, risk, safety
Method:
Description:
FMEA (failure mode and effect analysis) is a multidisciplinary team method preventive analysis to minimize potential failures of a process, product or means of production. In other words it is prevention of technical risks.
Criticality (C) (also called risk priority number) is the result of the multiplication of the severity (S) (also called gravity) by the occurrence (O) (probability, frequency) by the detection (D):
C = S x O x D
Interests:
Make the right decisions to reduce risks.
Design right the first time.
Produce right the first time.
Reduce machine downtime.
Improve internal communication.

## Slide 8
Description:
Problem solving method. The fault tree analysis is a tool for analyzing a combination of events.
The fault tree study is a deductive analysis (unlike the FMEA which is rather an inductive analysis) because it begins with the undesired event (in the example in red) and down to the basic causes (in blue). This requires going through the intermediate events (in green) and their logical combinations (yellow).
Interests:
The fault tree analysis allows:
to get an overview of potential problems and their interactions
to precisely define the probabilities of occurrence of various events and causes
To apply in the design appropriate technical solutions
To select the appropriate actions
1
Build the team. Determine the unwanted situation
Ask the question, "How and why? " several times
Group the responses per branch
Ask the question by branch to the root cause
Rank the responses and analyze the entire tree
Find priorities, plan and implement the action plan
2
3
4
5
6
7 FTA, fault tree analysis
problem, risk, safety
Method:

## Slide 9
Description:
HACCP = Hazard Analysis Critical Control Point.
Method, system of analysis and control of threats to food safety. HACCP is a preventive approach:
a multidisciplinary team hazard analysis
the establishment of effective countermeasures
the monitoring of actions
verifying the effectiveness of the system
Interests:
Prevention is based on critical limit not to be exceeded. The hazards are identified and controlled at every stage of production.
  8 HACCP
problem, risk, safety
1
Identify and analyse the hazards and critical steps
Identify the critical control points (CCP)
Establish control of CCP critical limits to monitor hazards
Introduce monitoring procedures on every CCP
Implement corrective actions if critical limits are exceeded
Check the effectiveness of hazard control measures
2
3
4
5
6
Keep register and build the HACCP folder
7
Principles:

## Slide 10
Description:
HAZOP (Hazard and Operability Study) is a hazard and operability study. Technique used by a multidisciplinary team to evaluate and address risks of complex systems. Toolkit for identification and analysis of risks and differences between planned and realized performance.
As the FMEA the HAZOP method analyses failure modes, their effects and causes but also identifies undesirable deviations from the predicted effects through guide words (too much, too late, too little, more, less, in part).
Interests:
Fosters team spirit.
Identifies the cause of a potential human error and limits the consequences.
  9 HAZOP
problem, risk, safety
1
Build the team. Approve the necessary resources
Define the scope of the study and the guide words to use
Set the objective to achieve. Go and collect field data
Identify activities included in the study
Ask questions with guide words to find the potential unwanted gaps
Determine the cause and consequence of each case of unwanted gap
2
3
4
5
6
Plan an action plan to eliminate or reduce potential gaps
7
Method:

## Slide 11
5. Self-actualization
3. Social
2. Safety
1. Physiological
4. Esteem
Description:
Tool showing the priority of human needs and motivational factors. Under normal conditions all need up of the pyramid can only be met if the above needs are met. Dissatisfaction of first two needs is demotivating. The other three needs are motivating conditions. It's not worth talking about motivation, respect, involvement if the staff is cold, hungry or not feeling safe. Any satisfied need ceases to be motivating.
Interests:
Prior to involve staff in a QCDSE approach (Quality, Cost, Deadline, Security, Environment) start by identifying staff needs (surveys, interviews).
Plan actions to respond to a maximum number of needs.
  10 Maslow’s pyramid
problem, risk, safety
Personal achievement, self-fulfillment
Self-respect from management, colleagues. Recognition of its ideas and actions
Participation in a group, integration and membership in a team
Safety and health, climate workshop, hazards protection
Hunger, thirst, clothes, hygiene, housing, wages
Examples:
5
4
3
2
1

## Slide 12
Description:
The PESTEL analysis is a strategic tool to find trends in macroeconomic factors that may influence the sustainability of the business.
Interests:
Allows to anticipate comprehensively the risks and opportunities of the business environment.
  11 PESTEL analysis
problem, risk, safety
1
Build the team. Set the list of PESTEL factors
Sort for each axis positive factors and negative factors
Considering the possible impacts analyze all factors
Release the environmental evolution of trends on each axis
Use trends as a database for strategic decisions
2
3
4
5
Method:
Policy:
National environment (taxation, subsidies), International (PAC, monetary policy)
Economy: Purchasing and spending power of customers and suppliers Social: Age pyramid, lifestyle, health Technology:
New technologies, innovation, research and development, patents
Environment:
Ecology, raw materials, cost of energy, recycling, clean energy
Legislation:
Industrial property, labor law, standards, contract law, customs

## Slide 13
Description:
Table form tool allowing at the beginning of a project to identify the hazards, the situations, the potential risks.
A 1 to 5 assessment criterion is defined for the probability of occurrence and severity of consequences.
The hazards are prioritized.
Recommendations to eliminate or reduce the most important hazards are determined.
Interests:
Identify and classify hazards by importance.
Determine recommendations to reduce potential hazards with respect to the causes, severity or favourable conditions.
12 Preliminary hazard analysis
problem, risk, safety
1
Build the team. Set the evaluation criteria
Identify all potential hazards
Determine for each hazard a note for its probability of occurrence and severity of consequences. Sort dangers.
Analyze the characteristics of each hazard
Establish recommendations to eliminate or reduce hazards in priority
2
3
4
5
Method:
Hazard | Cause | Effet | Favorable conditions | Occurrence probability | Severity of consequences
1 |  |  |  | 4 | 5
2 |  |  |  | 4 | 2
3 |  |  |  | 2 | 3
4 |  |  |  | 2 | 2
5 |  |  |  | 1 | 2

## Slide 14
Description:
Problem solving method. Discover the root cause of any undesirable event in order to eradicate it definitively.
Multidisciplinary team tool on the field.
Combine the benefits of other tools such as:
Brainstorming
WWWWHHW
5 W
5 M
Search among all possible causes the one which is good without fear to experiment.
Interests:
Foster teamwork and employee involvement.
Prevent a recurrence of the problem.
Strengthening customer confidence by informing him on actions taken.
Share best practices in other services.
13 RCA, root cause analysis
problem, risk, safety
1
Build the team. Define the problem
Establish the context of the problem on the ground. Collect data
Identify root causes
Analyze the causes and plan the action plan (responsible, deadline, resources)
Implement the actions. Try, if necessary, several times
Check and monitor the effectiveness of actions
2
3
4
5
6
Analyze results. Share best practices
7
Method:

## Slide 15
Description:
This method allows to discern the major risks. For every risk an index is established for the impact (I) and the likelihood of occurrence (L). The risk level (RL) is the result of the multiplication of the two indexes:
RL = I x L
For impact indexes from 1 to 5 can be used: negligible, low, moderate, high, critical.
For likelihood indexes from 1 to 5 can be used: unlikely, rare, occasional, frequent, very frequent.
The assessment of risk level is:
acceptable (green, 1 to 4)
minor unacceptable (yellow, 5 to 9) - means of control
unacceptable major (red, 10-25) - prevention to eradicate
Interests:
Groups the health and safety risks at work and environmental impacts.
Allows to analyze the risks and to take preventive measures.
Sort and clearly see the level of risk and inform and involve all staff.
Focus efforts on unacceptable risks.
Find and implement actions to mitigate risks and reduce them to an acceptable level.
Management is committed to supporting actions and allocate resources.
  14 Risk level
problem, risk, safety
1
Build the team. Identify the hazards and assess risks, known and potential
Establish impact and likelihood of occurrence indexes for each risk
For each non-acceptable risk establish an action plan (control means, prevention)
Implement the actions. Check that all risks have become acceptable
2
3
4
Method:

## Slide 16
Description:
Scenario analysis is a tool to identify and assess the risk of developing a dangerous situation in a more or less near future.
In different scenarios all potential consequences, severity and probability of occurrence are considered and analyzed.
Interests:
Be able to consider the different likely and future consequences.
Adapt better anticipating the evolution of risks.
Make the right strategic decisions.
  15 Scenario analysis
problem, risk, safety
1
Build the team. Define the problem
Establish the current risk (actual data)
Identify key trends and factors that may have an impact
Analyze each trend, its importance, uncertainty, level of control
Set the likely scenarios of potential changes
Evaluate each scenario compared to predictable factors (best and worst possible case)
2
3
4
5
6
Update scenarios regularly
7
Method:

## Slide 17
Description:
From Structured "What If" techniques – a "What would happen if?“ method.
Quick tool for identifying risks. Considered as a simpler variant than HAZOP method.
Find the effect of potential gaps by asking several times questions such as "What would happen if ... and what would be the consequences? ".
Analyze the risks and consequences of certain changes before their implementation.
Interests:
Simple, fast and universal method.
Allows to see how a system might react to certain gaps.
Allows to find opportunities for improvement.
Fosters team spirit.
  16 SWIFT
problem, risk, safety
1
Build the team. Define the problem and its scope
Establish the initial context (data collection)
Ask questions in the conditional tense on risks, known requirements and constraints
Rank the hazards and risks found by priority
Analyze the causes and consequences of risky situations
Establish an action plan. Implement the actions.
2
3
4
5
6
Verify the effectiveness of actions. If necessary repeat analysis
7
Method:

## Slide 18
Description:
From Strengths, Weaknesses, Opportunities, Threats.
Analysis and support tool to make an important decision. In the SWOT matrix in the left column (S, O) are the positive factors and in the right (W, T) the negative factors. The upper line (S, W) includes internal elements (easy to control) and the lower line (O, T) the external elements (more difficult to control).
Interests:
Find opportunities using the internal forces.
Overcome its weaknesses and address threats.
  17 SWOT analysis
problem, risk, safety
1
Build the team. Define the problem
Establish initial context, collect data
In each cell list the priority items (factors)
For the strengths and weaknesses consider the implications of process and key skills
For opportunities and threats consider the impacts of all stakeholders
Analyze the causes and consequences of each factor in detail
2
3
4
5
6
Save result as a database for strategic decisions
7
Method:

## Slide 19
Description:
The single document is mandatory since 2001 for every employer (in France). This document includes "the result of the evaluation of risks to health and safety of workers". The goal is to identify the risks associated with each workstation and to find measures to eliminate or reduce these risks.
Columns 1 to 4 relate the risk analysis.
Columns 5 to 7 relate the risk assessment (L = O x S)
Columns 8 to 11 relate the action plan.
Interests:
Indispensable tool for the prevention of occupational risks.
Fosters the involvement of all staff.
  18 The single document
problem, risk, safety
1
Build teams. Define a program of meetings
Identify all the activities with a potential risk in each workstation
List and assess each risk (level of risk)
Analyze unacceptable risks, determine the measures to be taken and establish an action plan
Implement the action plan. Check the effectiveness of actions (internal audits)
Hold the single document available to stakeholders
2
3
4
5
6
Update the single document annually or after any significant change
7
Method:
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Activity | Context | Risk | Conse-quence | Occu-rrence (O) | Seve-rity (S) | Level (L) | Measures | O’ | S’ | L’

## Slide 20
Description:
Problem solving method. The WWWWHHW comes from the words: what, who, where, when, how, how much, why. Tool to collect data before searching for causes.
Simple method to examine a problem from all possible angles, asking questions without moderation.
You can also use the verb in the conditional tense (should) and the word else (e.g., "who else should be involved?").
Negative questions can also be used (e.g. “who is not concerned?").
Interests:
Do not forget anything.
Quickly and easily find the data of a problem.
Facilitates the establishment of an action plan.
Fosters listening to others.
What?
What is it about ?
Who is affected?
Who does what ?
Where has this happened?
When has this happened?
How did that happen?
How many times has this happened? How much does that cost?
Who?
Where?
When?
How?
How much?
Why is this a problem? Why should we treat it?
Why?
  19 WWWWHHW
problem, risk, safety
Questions to ask: