## Slide 1
Lean tools
Lean
General:
Many of the tools in the Lean family come from the Toyota model (SMED, pull system, Kanban, Heijunka), while others are fully-fledged philosophies such as Kaizen, 5 S or Theory of Constraints. QCDSE stands for Quality, Cost, Deadline, Safety and Environment.
List of tools:
5 S
CTQ, Critical To Quality analysis
Andon
VSM, Value Stream Map
Hoshin method
Fail safe device (Poka-yoke)
Kano model
Spaghetti diagram
Pull system
Heijunka
Kaizen
Kanban
TPM, Total Productive Maintenance
Visual management
Gemba walk
SIPOC, Supplier, Input, Process, Output, Customer
SMED, Single Minute Exchange of Die
Standard
BSC, Balanced Scorecard
Takt time
Lean temple
TOC, Theory Of Constraints
OEE, Overall Equipment Effectiveness
Value added for the customer
VOC, Voice Of the Customer

## Slide 2
  1 5 S
Lean
Description:
Method to learn to control the order and cleanliness in the workplace, to build confidence, have a clear mind and work calmly. From Japanese seiri, seiton, seiso, seiketsu and shitsuke (sorting, setting in order, shining, standardizing and sustaining
Interests:
Draw attention to the problems.
The time to find a tool or document is minimized.
Each workspace becomes clean, pleasant, secure and ergonomic.
Space released. The workplace becomes a showcase.
S1
Sort
Save space?
Sorting identifies and unclogs anything that is not really useful
Find a tool in less than 10 seconds?
By setting in order, we tidy up and organize our workspace optimally
Ensure a clean and ergonomic workplace?
Shining improves the appearance of your workspace, it becomes more user friendly and any anomaly is more easily seen
Avoid reinventing the wheel?
By standardizing the first 3 S, we keep the good results obtained and we ensure the order and maintenance of cleanliness
Preserve lessons learned?
By sustaining, we encourage rigor and we acquire good habits. To question yourself regularly
S2
Setting in order
S3
Shine
S4 Standar
dize
S5
Sustain
Questions to ask yourself:

## Slide 3
2 CTQ, Critical To Quality analysis
Lean
Description:
The critical to quality analysis is a tool for understanding customer expectations.
Transform customer needs and requirements into internal requirements.
Find out what can influence the customer's dissatisfaction. Do not hesitate to ask them for details.
Interests:
Have a global idea of the quality perceived by the customer.
Transparent communication with customers.
Do not forget an essential step in a flow diagram.
Identify potential problems.
Find process improvement opportunities in time to better satisfy the customer.
1
Build the team. Define the limits of the analysis
Collect detailed information of critical process steps for quality (perceived quality by the customer)
Analyze internal requirements at the steps essential to quality
Determine how to measure the perceived quality by the customer
Choose improvement actions to better meet customer requirements
Put in place actions of essential improvements to the quality
2
3
4
5
6
Verify that the output elements of the process are adequate to the customer's requirements
7
Methodology:

## Slide 4
  3 Andon
Lean
Description:
Signal or luminous table that indicates the status of the process and alerts in case of problem, Japanese light.
Part of the Jidoka pillar of the Lean temple.
The signal is activated automatically by the equipment or manually by the operator in cases such as:
doubt about an operation
equipment malfunction
delay
Stop a section of the production line to immediately find the root cause.
Interests:
React quickly as soon as a problem appears.
Training on the workstation.
Promotes the autonomy and self-quality of each operator.
Average time between machine stops reduced.
In a workshop with dozens of pieces of equipment, the defect is immediately spotted.
1
Identify equipment that does not have an automatic or manual alarm signal
Choose the most appropriate way for each piece of equipment
Validate the necessary resources
by top management
Set up new alarm means
Test the correct operation of each alarm means
2
3
4
5
Methodology:
Write the instructions for using the alarm means
6
Set up the reaction procedures to the different problems
7

## Slide 5
4 VSM, Value Stream Map
Lean
Description:
A global communication tool (visual management) in A 3 format, created by hand in the field. Create a current map of the company's value streams (information, process activities, topics, people).
Then build a map of future value streams to find opportunities for improvement, such as reducing lead time.
Interests:
Obtain a global view of the flow of a product in the company and decide, in all transparency, the improvements to achieve.
Identify and reduce non-value-added activities, bottlenecks, sources of waste.
Show the links between the material flow and the flow of information.
Future map is also used before modifying an activity.
1
Build the team and designate the owner. Choose a key product (high turnover)
Establish the initial context of field flows starting with delivery (diagnosis)
Define the steps of the product and information flows
Identify value-added activities for the customer
Identify non-value-added activities for the customer
Analyze flows and find opportunities for improvement
2
3
4
5
6
Build future map (vision). Note the date
7
Methodology:
Put in place the improvements. Update the future map regularly
8

## Slide 6
  5 Hoshin method
Lean
Description:
The Hoshin method (also known as Kaikaku or Kaizen Blitz, from German lightning) is a multi-disciplinary team activity to improve the performance of a concrete common project in a defined area within a period of time, limited to one to two weeks.
Do not confuse with Kaizen.
Focusing on the collective effort of rapidly changing a situation where non-value-added is noticed, using the PDCA cycle.
Interests:
Helps to find a durable solution in a relatively short time.
Pooling of good practices.
Commitment and active participation of top management.
Promotes team spirit, communication and creativity.
1
Build the team, release the daily tasks, name the leader. Define the site
Establish the current context in the field (including safety instructions)
Define the objective to achieve ("ideal" situation), the tools to use
Identify waste and opportunities for improvement. Take into account the constraints
Plan the operational activities
Set up the activities. Try, if necessary, a few times
2
3
4
5
6
Check the effectiveness of the actions. Pool the good practices
7
Methodology:

## Slide 7
6 Fail safe device (Poka-yoke)
Lean
Description:
Simple anti-error equipment to avoid and not allow to produce nonconformities. From Japanese Poka - error, and Yoke - avoid.
Poka-yoke is a tool for prevention and also problem solving. It is much more effective than other methods because it attacks human error as an unpredictable root cause.
Interests:
An inexpensive, often very simple (DIY trick), the Poka-yoke can successfully fight against human errors especially where the tasks are monotonous.
Do not let any error go to the next step.
Quickly understood and accepted because it is based on common sense.
1
Build the team including with operators. Define the potential error
Establish the initial context in the field
Set the objective to achieve
Identify possible solutions
Choose the best solution and plan the implementation
Set up the solution. Check the operation and its effectiveness
2
3
4
5
6
Pool good practices with other equipment
7
Methodology:

## Slide 8
  7 Kano model
Lean
Description:
Customer satisfaction survey data is the basis for making the Kano chart. It is a visual method to realize the customer’s level of satisfaction with their expectations.
Customer expectations (which change over time) may be mandatory (basic), proportional (performance) or attractive (seductive).
Interests:
Set priorities to meet customer expectations.
Understand how a function is perceived by the customer.
1
Define the key functions of the product
Identify the relevant questions with 5 possible answers (such as "How much does the abc function meet your expectations?")
Send the questionnaire to customers. Analyze customer responses
Draw the results on the graph
Determine the improvement tracks by function and by expectation
Focus your efforts on attractive expectations
2
3
4
5
6
Implement an action plan
7
Methodology:

## Slide 9
  8 Spaghetti diagram
Lean
Description:
The spaghetti diagram is a graphical tool showing the physical flows (personnel and materials) in a production area.
Starting point to improve the performance of the process.
Use with 5 S tools and value stream mapping.
Interests:
Visually represent all flows to facilitate waste hunting.
Optimize certain activities, simplify flows.
Reorganize the layout of machines and production lines to reduce waste.
1
Build the team. Define the area. Use the site plan of the area
Establish storage locations for products, tools, consumables
Notify staff and draw flows of people and products (in and out)
Set the goal to reach (such as decrease unnecessary transport by 30%)
Analyze the flows (brainstorming) and find the possible improvements. Simulate on paper versions
Put in place the best solution
2
3
4
5
6
Check the achievement of the goal. Pool good practices
7
Methodology:

## Slide 10
  9 Pull system
Lean
Description:
The push flow is the classic production (the forecast determines what we will produce). The pull flow is lean production (produce only what is requested, only when it is requested; the salesperson orders the production).
Interests:
Immediately raise the problems to the surface.
Production directly related to the customer's request. No scheduling.
Continuous flow, stocks are standardized and in small quantity, the reconstitution process is controlled visually (Kanban).
Minimal cycle time and lead time. Reduced waste (and costs).
1
Stabilize the processes. Extend standards at every level
Make a map of current value flows
Analyze the different flows (of information, processes, products, people)
Establish a map of future value streams
Smooth the organization of the lines according to the "takt time" to obtain a continuous flow
Set up inventory management by label (Kanban)
2
3
4
5
6
Level production according to customer demand
7
Methodology:

## Slide 11
  10 Heijunka
Lean
Description:
Heijunka is a method of smoothing production by optimizing the flow of different products.
Prerequisites:
quick change of products series (SMED)
very low level of nonconformities
pull system, Kanban cards
operator flexibility (multiple skills)
The sequence of production is regularly reviewed in relation to the daily evolution of the customer's request using the Kanban card box.
Interests:
Workflow directly related to customer demand.
Reduced lead time.
Every product is made and available every day:
the customer is delivered the same day
pending products are greatly diminished
The use of people and machines is better distributed.
Orders to suppliers are stable and regular.
1
Identify the total quantity to be produced, for example, over a week
Optimize fast change of series (SMED)
Check the actual capacity for each product
Organize the production sequence to produce each product each day
Test and set up the best organization
Standardize documentation
2
3
4
5
6
Modify as soon as an evolution of the customer's request appears
7
Methodology:

## Slide 12
  11 Kaizen
Lean
Description:
The Kaizen approach is the backdrop of the Lean temple. From Japanese Kai (change) and Zen (good) or continual improvement (step by step) as a state of mind. Philosophy developed and diffused in the world by Masaaki Imai. Do not confuse with the Hoshin method.
Kaizen essentials:
5 S (improve working conditions)
eliminate waste
standardize (set up and improve regularly)
Concepts used in Kaizen philosophy:
teamwork
the PDCA cycle
visual communication
not a day without an improvement
consider the next step as a customer
quality and the process approach before the results
rely on field data
control variability
massive formation
promote common sense
Interests:
Eliminate the causes of variation and standardize the results to eradicate known problems.
Find the conditions for staff development at work.
The hunt for waste enters the culture of the company.
Low costs of improvements.
The suggestions are many and varied.

## Slide 13
  12 Kanban
Lean
Description:
From Japanese production order card or label. To be able to produce everything and all the time. Inventory management by cards or cards attached to product boxes to operate in a pull system.
Essential element of the "Just in Time" pillar of the Lean temple.
Replenishment of workstations stalled at the request of the customer (next post) is driving with the eyes.
Prerequisites: SMED, stable process, minimal level of defects, continual flow, personnel strictly respecting the established rules.
Interests:
Visualize the workflow and hidden waste.
Smooth the production.
Increase flexibility.
Stocks and storage space reduced.
Improve continually (number of Kanbans).
Promotes team spirit (autonomy, self-quality).
1
Build the team. Define the product and the steps
Set the quantity of products per box
Set the volume of the supermarket
Calculate the number of Kanban cards needed
After a few tries implement Kanban cards
Check the effectiveness of the cards and optimize their number
2
3
4
5
6
Review Kanban cards at least once a month
7
Methodology:

## Slide 14
  13 TPM, Total Productive Maintenance
Lean
Description:
Set of preventive measures of treatment of the causes of failures of the realization machines.
Maintenance is planned against past failures.
The principle of prevention is generalized.
The staff (those who do) are trained in daily maintenance.
Interests:
Decrease the cost due to machine downtime.
Increase the life of equipment and machinery.
Eradicate major breakdowns.
Guarantee equipment and machines availability, performance and flawless safety.
1
Collect the failure history of an equipment family
Analyze the root causes, calculate the overall equipment effectiveness (OEE) and the average time between two failures
Define priorities (major failures)
Identify the critical components. Identify the optimal conditions
Train the staff in the daily self-maintenance program
Clean and inspect critical components
2
3
4
5
6
Develop standards and share best practices
7
Methodology:

## Slide 15
  14 Visual management
Lean
Description:
Visual management is an essential method of the Jidoka pillar of the Lean temple.
Visual means often updated to see at a glance:
achievement of objectives
the appearance of a nonconformity (Andon)
the inventory of current actions
the last proposals (A 3)
the procedure to follow
Interests:
From the beginning, all problems are exposed.
Real-time performance information is available to all staff (awareness, motivation).
Promotes team spirit, respect for deadlines, reduces mistakes and defects.
Visual reminder of the rules on the workstation (standardization, security).
1
Build the team. Define the area of activity (workshop area)
Define the essential goal to reach
Analyze and choose the means to use (simple, visible, understandable)
Put the different visual means in the right places
Define the managers for daily monitoring of each means
Check the effectiveness of the actions once a week
2
3
4
5
6
Analyze the results. Pool good practices
7
Methodology:

## Slide 16
  15 Gemba walk
Lean
Description:
Gemba comes from Japanese "the place where it happens".
Walk to Gemba every day to learn to see, understand and react.
Interests:
Direct relations with the staff. Understand their worries. Put safety always in the foreground. Learn to observe and see with Lean eyes.
Review of performance indicators in the field.
Motivated staff because they are not afraid to make suggestions for improving the work environment.
From the appearance of a problem, we are together on the ground to find the best solution.
1
Go to the field (Gemba)
Learn to see. Ask yourself the right questions
Look at the process and observe what is happening now
Ask the right questions to the right people
Collect current facts, analyze them and identify the root causes
Put in place the necessary actions (PDCA)
2
3
4
5
6
Pool good practices
7
Methodology:

## Slide 17
  16 SIPOC
Lean
Description:
Used in phase D (Define) of the DMAIC tool. Define the process, set objectives, identify what is important for the customer. Consider at this stage the process as a black box with its inputs and outputs.
Interests:
Identify the expectations, needs and essential requirements of the customer.
Find consensus on the area and limits of the process.
Determine and analyze the inputs and outputs of the process.
Compare the inputs and outputs of the process with the possibilities of the supplier and, especially, the expectations of the customer.
1
Build the team. Define the domain and activities of the process
Compare process inputs with critical supplier elements
Compare the outputs of the process with the expectations of the direct customer and the end customer
Identify the key elements that can influence the process, the outputs and the customer
2
3
4
Methodology:

## Slide 18
  17 SMED
Lean
Description:
From English, Single Minute Exchange of Die, series change in less than 10 minutes.
A method of organizing the activities of a line or equipment to significantly reduce the time between two sets of products. Example: changing tires in Formula 1!
Use trolleys for tools. Keep tools in perfect condition at all times. Add benchmarks on tools. Use electrical tools.
Interests:
Decrease the lead time of a product.
Reduce the size of the batches.
Use of resources (people and material) optimized.
1
Build the team. Define the topic
Evaluate the initial context in the field before, during and after the change (list of operations, tools, materials, people)
Define and measure the time of internal operations (during the change - as machine stops)
Define and measure the time of external operations (before or after the change - preparation and storage of tools)
Transform as many internal operations as possible into external (preheat mold)
Improve internal operations (reduction, adjustment) and decrease external operations
2
3
4
5
6
Check the effectiveness of the improvements. Mutualize good practices
7
Methodology:

## Slide 19
  18 Standard
Lean
Description:
The standard is a work instruction, a procedure, showing the safest, simplest, easiest and most efficient way to perform an operation. Goal:
work safety
do it well first time and every time
use the best method for each repetitive job
Is not fixed, resumes progressively after improvements are found and verified.
Standardized work is easy to understand and respect by everyone involved in its creation and improvement.
Interests:
Increases the performance of operations and the pride of a job well done.
Facilitates the training of newcomers and the versatility of staff.
Promotes self-quality and team spirit.
Waste and variability are reduced.
1
Build the team including with the operators
Establish the initial context in the field, the beginning and the end, tools, materials, requirements
Define the objectives to be achieved, the risks and the unavoidable constraints
Analyze work, choose the best suggestions and optimize tasks
Check the cycle time. Write down the key points. Keep it simple. Use best practices
Visibly implement work standards. Train new operators
2
3
4
5
6
Check the effectiveness of the standards. Regularly improve standards with operators
7
Methodology:

## Slide 20
  19 BSC, Balanced Scorecard
Lean
Description:
The Balanced Scorecard (BSC) reflects the company's vision and purpose in four strategic areas (finance, customers, people, processes).
To drive these 4 axes and obtain a balance, an action plan is built with objectives and key performance indicators.
Interests:
Successful communication from top to bottom.
Make decisions based on the long term.
Allows to question its strategy and to realize if the balance between the strategic axes is maintained.
1
Validate the strategy at the management committee. Define the strategic objectives. Allocate the necessary resources
Establish balanced indicators for financial results (turnover, margin)
Establish balanced indicators for customer satisfaction (satisfaction rate, new customers)
Establish balanced indicators for people’s development (number of candidates, hours of training)
Establish balanced indicators for mastering key processes (overall equipment effectiveness)
Determine the relevant tactics. Implement key performance indicators
2
3
4
5
6
Follow and improve the strategic dashboard
7
Methodology:

## Slide 21
  20 Takt time
Lean
Description:
The takt time (from German - rhythm) is the available time in production divided by the customer demand for a specified period (usually a day).
Main tool for smoothing orders in production to improve the balancing of lines.
Used in the mapping of value flows.
It is a method of improving the rate of production.
Interests:
Produce at the fairest.
Reduce waste.
Shows opportunities to improve the process.
Reduce bottlenecks.
1
Build the team. Define the area to be improved
Establish the initial context in the field
Set the goal to reach
Identify the longest operation (bottleneck)
Analyze the constraints of the process. Balance the operations
Calculate the new takt time
2
3
4
5
6
Check whether the goal is reached. Pool good practices
7
Methodology:

## Slide 22
  21 Lean temple
Lean
Description:
The Lean temple symbolizes the Toyota spirit.
The foundation includes essential approaches to quality control, such as:
respect for the staff
leadership, problem solving and training, pride in the work done, a good atmosphere in which to work together, taking into account the company's culture
operational stability, process simplification, smoothing
standardized work, the 5 S, reduction of variability
flow optimization
self-quality
Just in time, the first pillar of Lean, includes pull production, SMED, Kanban and takt time.
The Jidoka, the second pillar of Lean, includes automatic shutdown from the first nonconformity, the fail safe devices (Poka-yoke).
In the backdrop of the Lean Temple is the Kaizen approach with principles like continual improvement and the hunt for waste.
The roof of the Lean Temple contains the QCDSE axes.

## Slide 23
22 TOC, Theory Of Constraints
Lean
Description:
The theory of constraints was developed by Eli Goldratt and diffused in the world thanks to its novel "The goal".
A constraint is a resource with the highest load.
A bottleneck is a resource that is unable to meet current demand.
Thoughts of the theory of constraints:
Balance the flow, not the capacity.
An hour lost in a bottleneck is lost time for the whole system.
The constraint governs the product of sales.
An hour saved in a non-bottleneck is just a mirage.
The process batch must be variable and not fixed.
1
Build the team. Identify the constraint (highest stock level at entry)
Establish the initial context in the field
Identify the characteristics of the constraint
Carefully analyze the optimal conditions for the constraint
Decrease the constraint (increase its flow)
Subordinate all other processes to the constraint
2
3
4
5
6
Repeat if another constraint appeared
7
Methodology:
Interests:
Increased flow so increased profits.
Fewer stocks, so less waste.

## Slide 24
23 OEE, Overall Equipment Effectiveness
Lean
Description:
The OEE (Overall Equipment Effectiveness) is an indicator of machine utilization with which the efficiency of a production line used in total productive maintenance is measured.
The OEE is equal in percentage to the availability multiplied by the performance multiplied by the quality:
OEE = AxPxQ (%)
A is the % of the useful time (total time decreased by breakdowns, maintenance, change of series).
P is the % of the operating time compared to the useful time.
Q is % of compliant (normal) parts compared to the parts produced.
Interests:
Identify categories of production losses.
Facilitates the implementation of actions to increase the efficiency of a production line.
1
Build the team. Define the area to be improved
Set the initial context in the field. Calculate the OEE
Define the goal to reach and set the priorities
Categorize production losses into categories (availability, performance, quality)
Analyze the root causes and plan an action plan
Set up the actions. Try, if necessary, a few times
2
3
4
5
6
Check the effectiveness of the actions. Pool good practices
7
Methodology:

## Slide 25
  24 Value added for the customer
Lean
Description:
The activities of a company can be classified into 3 types:
value added (VA) for the customer
non-value added (NVA) for the customer but necessary
without any value added (AVA) for the customer (pure waste)
Interests:
Identify, simplify, reduce and eliminate activities without VA for the customer.
Decrease the lead time.
Increase customer satisfaction
1
Build the team. Define the area to be improved
Establish the initial context in the field
Set the goal to reach
Identify activities with VA, NVA and AVA for the customer
Analyze each activity. Choose actions to reduce and eliminate activities without VA for the customer
Set up actions to reduce and eliminate activities without VA for the customer
2
3
4
5
6
Check the effectiveness of the actions. Pool good practices
7
Methodology:

## Slide 26
  25 VOC, Voice Of the Customer
Lean
Description:
The voice of the customer (VOC) is a way to understand what is important to the customer.
It is a tool for determining priorities in relation to the needs and expectations of the customer.
It's an attitude to establish how best to meet customer expectations.
Interests:
Know and understand the expectations and needs of the customer.
Identify opportunities for improvement.
Increase the added value for the customer.
1
Build the team. Define resources (people and time)
Establish priority customers and products
Collect existing data and conduct targeted interviews
Analyze all the data
Determine priorities by customer and product. Formalize the results
Put actions in place to better meet customer expectations
2
3
4
5
6
Check the effectiveness of the actions. Share the results with all staff
7
Methodology:
Some of the most used means:
Kano diagram
critical to quality analysis
customer complaint analysis
customer feedback analysis
customer satisfaction survey
interviews
visit to the customer
customer visit in the company